## Slide 1: Voice Command Based Object Identifying Robot using Speech and Image Feature Extraction
Project Members:
Kanhaiya Lal Shrestha 069BEX417
Dipkamal Bhusal 069BEX414
Bishal Lakha 069BEX410
Bishal Heuju 069BEX409
Project Supervisor:
Dr. Nanda Bikram Adhikari

## Slide 2: TABLE OF CONTENTS
1. Motivation
2. Introduction
3. Application
4. System overview
5. Methodology
  Speech recognition
  Object recognition
  System implementation
  6. Experiments
  7. Problems encountered
  8. Conclusion

## Slide 3: MOTIVATION
Development of general-purpose service robots
Interfacing hearing and vision to an embedded system

## Slide 4: INTRODUCTION
Robots intelligent enough to understand speech and recognize object
Interfacing two human senses, hearing and vision to machine
Speech signal to command robot
Robot able to identify and track the object
Proof-of-concept of assistant robot

## Slide 5: APPLICATION
Home assistant robots
Standalone systems can make use of speech recognition and computer vision

## Slide 6: SYSTEM OVERVIEW
I/O
Processing
Image Acquisition
Object Recognition
Remote Controlled
Camera
Real World Robot Movements
M
M
Human to Machine Interface
Voice Command
Machine to Human Interface
Speaker
Voice Recognition

## Slide 7: METHODOLOGY

## Slide 8: SPEECH RECOGNITION
Isolated word
Pattern recognition approach

## Slide 9: PATTERN RECOGNITION-TEMPLATE METHOD
Get feature vectors
MFCC
Train voice signals
Match feature vectors between train and test signals
Command recognized
Get feature vectors
Test voice signal
MFCC

## Slide 10: FEATURE EXTRACTION

## Slide 11: MFCC
Based on the known variation of the human ear’s critical bandwidth with frequency
Speech
Pre-emphasis
DFT
Framing
Windowing
Mel filter bank
Discrete Cosine Transform
Output
Delta Energy and Spectrum

## Slide 12: TRAINING
System trained to store the reference MFCC features
System uses the pyAudio library to take an input sample .wav file
System trained to recognise two words; IDENTIFY and FOLLOW

## Slide 13: FEATURE COMPARISON

## Slide 14: DTW
A time series alignment algorithm for measuring similarity between two temporal sequences which may vary in time or speed.

## Slide 15
Chart: Plot of two signals
X features | 1 | 1 | 2 | 3 | 2 | 0
Y features | 0 | 1 | 1 | 2 | 3 | 2 | 1

## Slide 16: Using Euclidean distance, we get the distance matrix and the shortest distance shows the level of similarity.

## Slide 17: RESULTS
MFCC feature extraction
DTW for comparison
Chart: Recognition efficiency of word IDENTIFY
Chart: 
RESULTS
17
Voice command based object identifying robot using feature extraction
Chart: Recognition efficiency of word IDENTIFY
| Hit | Miss
Recognition efficiency | 0.857 | 0.243
Chart: 
| Hit | Miss
Recognition efficiency of word FOLLOW | 0.8928 | 0.1072
Trained under 20 times

## Slide 18: OBJECT RECOGNITION
Identification of an object in the given image/video.
Object recognition system can tell if the given image contains a cup or a pen or other
Can be ‘Specific’ or ‘Generic’

## Slide 19: BAG-OF-FEATURES
Generic object recognition
Image is represented as a histogram of visual words
Involves Feature detection and description, Visual vocabulary formation and Classification

## Slide 20: KEY-POINTS DETECTION AND DESCRIPTION
Uses Speeded-Up Robust Transform (SURF) method
SURF combines Hessian keypoint detector with its own feature descriptor
Provides scale and rotation invariant descriptor

## Slide 21: SURF KEY-POINTS DETECTION FOR DIFFERENT HESSIAN THRESHOLDS

## Slide 22: VISUAL VOCABULARY FORMATION AND IMAGE REPRESENTATION

## Slide 23: K-MEANS ALGORITHM ILLUSTRATION
Randomly Chosen Cluster Centroid
C1
C2
C1
C2
New cluster centroids found using mean of each cluster

## Slide 24: CLASSIFICATION USING SVM
Support
Vectors
Margin
w.x + b = 1
Optimal line
If w.x + b > 1
x
If w.x + b < 1
x

## Slide 25: BLOCK-DIAGRAM
Bag of Words
SURF
Train Images
Train SVM classifiers
Maintain SVM’s parameters
Input test image
Extract feature vectors
SURF
SVM classifiers
Recognize the object
Learning part
Recognition part
K-means
K-means

## Slide 26: OBJECT TRACKING
Reference Rectangle
Near
Far
Right
Optimal Distance
Left

## Slide 27: OBJECT RECOGNITION RESULT

## Slide 28: OBJECT TRACKING RESULT

## Slide 29: SYSTEM IMPLEMENTATION

## Slide 30
Camera
Microphone
Motor Driver
M
M
Atmega32
Microcontroller
Bluetooth Module
Power Source
Servo Motors
S
S
Android Mobile Device
Raspberry Pi
Control System
Processing System
Input

## Slide 31: FLOW CHART

## Slide 34: EXPERIMENTS ON SPEECH RECOGNITION

## Slide 35: VARYING THE SIZE OF FEATURE VECTOR
Chart: Recognition efficiency of word IDENTIFY against different feature vector size
| 8 | 17 | 31
Hit | 0.2 | 0.857 | 0.4615
Miss | 0.8 | 0.143 | 0.5385

## Slide 36: VARYING THE SIZE OF FEATURE VECTOR
Chart: Recognition efficiency of word FOLLOW against different feature vector size
| 16 | 25 | 20
Hit | 0.625 | 0.95 | 0.8928
Miss | 0.375 | 0.05 | 0.1072

## Slide 37: VARYING SAMPLING RATE
Chart: Recognition efficiency of word IDENTIFY against different sampling rate and different trained vector size
| 48 KHz | 16 KHz | 8 KHz
8 | 0.2 | 0.33 | 0.2
17 | 0.857 | 0.5625 | 0.2
21 | 0.4615 | 0.6315 | 0.6

## Slide 38: EXPERIMENTS ON OBJECT RECOGNITION

## Slide 39: Object recognition efficiency without background
Chart: 
| Calculator | Key | Multimeter | Pen | Watch
Recognized | 6 | 8 | 4 | 8 | 7
False Recognition | 3 | 2 | 3 | 2 | 2
Unrecognized | 1 | 0 | 3 | 0 | 2

## Slide 40: Object recognition efficiency with background
Chart: 
| Calculator | Key | Multimeter | Pen | Watch
Recognized | 8 | 4 | 3 | 2 | 3
False Recognition | 1 | 3 | 1 | 6 | 2
Unrecognized | 1 | 3 | 6 | 2

## Slide 41: CONCLUSION
Implemented vision and hearing sense in a machine.
Robot identifies commands and the object shown.
It tracks the motion of the object identified.

## Slide 42: REFERENCES
G. Z. Z. S. F. Zheng, “Comparison of Different Implementations of MFCC,” Journal of Computer Science & Technology, vol. 16, pp. 582-589, 2001.
N. Batra, “Programatically understanding dynamic time warping,” [Online]. Available: http://nipunbatra.github.io/2014/07/dtw/. [Accessed July 2016].
N. T. a. M. C. Marc T.law, Bag-of-Words Image Representation: Key Ideas and Further Insight, Switzerland: Springer International Publishing , 2014.
H. Bay, A. Ess, T. Tuytelaars and L. V. Gool, “Speeded-Up Robust Features (SURF),” 2008.
S. R. Gunn, “Support Vector Machines for Classification and Regression,” Faculty of Engineering,Science and Mathematics School of Electronics and Computer, 1998.

## Slide 43: Thank You !